Overview

The following describes the bmsmot pcb design & layout at this stage of development (March 29 2023). The eagles files can be found in--
~/GliderWinchItems/bmsmot/hw/eagle/bmsmot

Only parts for the needed features can be installed, and the value of resistors, capacitors, etc., the following are tentative.

This board can be configured to handle the EMC/MMC or PSN Power Supply Node (PSN).

For the EMC/MMC the following is supplied
- BMS CAN 12v power switched
- BMS CAN Master Reset switched
- Contactor coil #1 energize
- Contactor coil #2 energize
- Contactor HV measurements
- Conatctor current measurements
- Cooling pump control (PWM)
- Heat exchanger fan/blower control (PWM)
- DMOC fan control (PWM)
- SCP 12v supply input on/off relay
- RCP 12v supply input on/off relay
- SCP 12v supply output relay on/off
- AC/DC input power select relay
- Coolant inlet temperature thermistor
- Coolant outlet temperature thermistor
- Ambient temperature

For PSN-
- Main 12v battery on/off
- Air compressor on/off
- Air pressure measurement (? ADC, but not SPI)
- AC voltage measurement
- Mains/generator select
- RTC wakeup

Other provisions-
- LEDs
     LED1 - Green: 12v switched power
     LED2 – Green: PB12 i/o-F446
     LED3 – Red: PB13 i/o-F446
     LED4 – Green: PB0 i/o- L431
     LED5 – Red: PB1 i/o-L431
     LED6 – Red: NFET5/PA5-Master Reset (BMS loop)
- EMC/MMC to EMC master UART-UART communication
- Pushbuttons
    RESET – F446
    RESET – L431
    Master-Reset BMS loop
- Header for encoder (TIM2)
- ADC:
   Four with 2 pin headers: 10K pullup w 0.1 cap to gnd
   +12v power measurement (no header)
   Two with 2 pin headers: Series resistor, 10K pullup w 0.1 cap to gnd
- spare ADC
- spare FET/relay outputs
- Xtals:Oscillators
   32 Khz RTC
   16 MHz system

Board size
140 x 100 mm
Mounting hole (dia 3.2 mm) positions--
     3.2 3.2
 136.8 3.2
 136.8 96.8
     3.2 96.8
   80.0 70.0

12v power input

(Upper-left) the 12v power is connected via a Power Pole connector pair with a pigtail, or spade lugs. There are two large holes for strain relief for the Power Pole option. The pigtail solders into holes in the middle of the spade lug thu-holes. This called the “raw” 12v power.

Possible power PFETs provide polarity protection--
DMP3007SCG-7
PJQ4403

The input voltage will exceed the Vgs for a DMP3007 so a 10v zener used. The PJQ4403 has a +/- 20 Vgs so the zener could be omitted, however the PJQ4403 has a lower continuous Id.

12V power protected

The polarity protected output of the input PFET is “+12V” on the schematic. This feeds into a second PFET that can switch the 12v on/off.

12V power switched

The switched 12v feeds the BMS CAN bus loop, and most of the BMS board.

When configured for a Power Supply Node (PSN) the 12v battery would power this board and if the second PFET is off the only load on the battery is the 5v regulator and processor. The processor would be in shutdown mode so its draw would be in the 1-10 ua range. The linear regulator is in 1.8 ua typical. To wake the system either a short to gnd via the 2-pin header JP19, or NFET1 turned on via the processor RTC and coin-cell.

Configured for the EMC/MMC the switched 12v can turn the BMS CAN bus 12v on/off via the NFET and i/o pin PC13.

would be if there are external loads on the SUBx outputs (more later on these). Such loads would likely be 12v relays and would not draw current when not active.

FET outputs (SUBx)

Eight FET driven outputs are labelled HDR-SUB1 through HDR-SUB8. Each output has a JST 4 pin keyed header (gnd, fet drain, +5v, +12v). Provision is for flyback diodes to 5v, 12v, and a pullup resistor. The FET, diode/resistor, installed depends on the usage of the output.

Each FET is driven from an i/o pin that can be assigned to a timer channel so that PWM can be applied. Some outputs share the same timer which means that the PWM frame duration would be common to all the channels on that timer doing PWM.

FET outputs (HDRx)

Four outputs driven by a 74VHCT125 buffers can drive external sub-boards with power fets for high current switching. These inputs to the buffers are i/o pins that have associated timers.

ADC ‘F446

Four inputs have 10K pullups and 0.1u cap to gnd for thermistors.

Two have a series resistor added which could be used for voltage divider by installing a resistor in place of the 0.1 cap. It could be used for input of an external switch or contacts; the 0.1 cap could be replaced with a zener if voltage protection is needed, etc.

Master-Reset

The BMS loop RJ45 jack pair OR the Master-Reset from the CAN1 bus, presumably pulled to gnd by the system CAN bus, and the NFET or pushbutton. The NFET can pull the Master-Reset for the BMS CAN bus loop to gnd without affecting the Master-Reset line on the CAN1 bus.

The pushbutton is mostly for sw debugging and test, and probably not worth installing on all boards. Pressing the pushbutton pulls the Master-Reset for the BMS loop to gnd, resetting all BMS boards on the loop. Other boards on the loop that have the Master-Reset feature would also be reset, but non-BMS boards on the loop are not contemplated.

Red LED6 lights when the BMS loop Master-Reset is pull to gnd.

Coin-cell and VBAT

A vertical socket for a CR2032 coin-cell (upper right corner of pcb) powers VBAT. When the coin-cell is present and the voltage is above 1.7v the RTC domain of the ‘F446 remains active when the processor power is off.

VBAT is internally connected with a diode to Vcc inside the processor so when the coin-cell is not installed the RTC section still works when the processor is powered, however it is recommended that when there is no coin-cell that VBAT be connected to VCC. No reason is given as to why this is recommended. One could speculate that given the extremely low current draw of the VBAT that a floating pin when the power is off might end up with some breakdown of internal circuits. A resistor (which could be zero ohm) to connect VBAT to Vcc is provided.

The RTC section when maintained by the coin-cell will run the 32 Khz clock, power a few i/o pins and power the backup registers (1K bytes). The RTC timer can be configured to have PC13 raise the NFET to switch the +12V on when there is a timeout. The NFET is OR’d with a 2 pin hdr so that a jumper or external switch will pull the power PFET gate down to turn on the +12v.

Isolated ‘L431

A STM32L431RxT6 processor is isolated from the system ground. Since the 5v-5v isolation is switcher and noisy (and the input to the dc-dc isolation switcher is also a switcher output) linear regulators are used to clean up the power. Two 5v-5v 1W convertors are used. The output of the two converters are connected in series to provide a nominal 10v which is linear regulated to 5v to provide a clean 5v for a Hall-effect current sensor. The first dc-dc converter output is linear regulated to drive the processor 3.3v and its ADC.

Provision is for four high voltage dividers to the ADC. The resistor to the high voltage is a thru-hole resistor as the working voltage spec requires ½ watt resistor.

For filtering, the HV resistor is 1M with a series 110K to the ADC pin with 10K ADC pin to gnd shunt. The 1M and 110K junction has 0.1u cap and the ADC pin has a 0.1u to gnd cap.

Header for Hall-effect (gnd, signal, +5) with the signal going through a filter of 0.1u-series 5.6K-0.1u-10K to with ADC pin with 0.1u to gnd.

A processor i/o pin driven red and green LED are for debugging/trouble-shooting.

The SWD and FTDI headers provide for flashing and debugging.

Isolated UART TX & RX is provided. The ‘L431-to-’F446 direction is necessary for streaming readings; the reverse direction might be used for possible program updating over CAN.

There is no control for the isolation limit????